## Slide 1: ARRAY MULTIPLIER

## Slide 2: CONTENTS
Requirement
Principle
Implementation and Simulation
Advantages and Disadvantages
Conclusion

## Slide 3: Requirement
As we know multiplication is an essential arithmetic operation. It makes easy in in finding squares , powers , also used for signal convolution in signal processing, used for image coding, filtering

## Slide 4: Principle
Serial Multiplication (Shift-Add)
  Computing partial products by anding multiplicand and multiplier bits bit by bit.
  Adding the partial products by multiplying each multiplicand with multiplier and shift to left by one bit for every multiplier bit.
  Add bits under same position must be added.

## Slide 5: 4*4 bit multiplication principle

## Slide 6: 4 – bit array multiplier block diagram

## Slide 7: Simulation & implementation
HALF ADDER MODULE :-
module HA(sout,cout,a,b);
output sout,cout;
input a,b;
assign sout = a^b;
assign cout=(a&b);
endmodule

## Slide 8
Full adder module :-
module FA(sout,cout,a,b,cin);
output sout,cout;
input a,b,cin;
assign sout = (a^b^cin);
assign cout=((a&b)|(a&cin)|(b&cin));
endmodule

## Slide 9: Multiplier Module :
module Arraymultiplier4bit(product,A,B);
input [3:0]A;
input [3:0]B;
output [7:0]product;
assign product[0]=(A[0]&B[0]);
wire c1,c2,c3,c4,c5,c6,c7,c8,c9,c10,c11,c12,c13,c14,c15,c16,c17;
HA HA1(product[1],c1,(A[1]& B[0]),(A[0]&B[1]));
FA FA1(c2,c3,A[1]&B[1],(B[0]&A[2]),c1);
FA FA2(c4,c5,(B[1]&A[2]),(B[0]&A[3]),c3);
HA HA2(c6,c7,(B[1]&A[3]),c5);
HA HA3(product[2],c15,c2,(B[2]&A[0]));
FA FA5(c14,c16,c4,(B[2]&A[1]),c15);
FA FA4(c13,c17,c6,(A[2]&B[2]),c16);
FA FA3(c9,c8,c7,(B[2]&A[3]),c17);
HA HA4(product[3],c12,c14,(B[3]&A[0]));
FA FA8(product[4],c11,c13,(B[3]&A[1]),c12);
FA FA7(product[5],c10,c9,(B[3]&A[2]),c11);
FA FA6(product[6],product[7],c8,(A[3]& B[3]),c10);
endmodule

## Slide 10: Simulation circuit

## Slide 11: Advantages & disadvantages
Advantages :-
  Minimum complexity
  Easily scalable
  Easily pipe lined
  Regular shape
Disadvantages :-
  High power consumption
  Large area requirement for scalability

## Slide 12: Conclusions :-
Array multiplier is simulated and implemented in Verilog
We can increase the performance using pipeline technique
Array multiplier has better performance than serial multiplication scheme.